## Slide 1
The Refrigerator, what is inside and how it works
Please notet that the functionality of this presentation depends on other files and that these are organized as follows:
In order to have the animations working, it is important that the PC on which the animations will run, has got Flash Player installed. All you have to do is to double-click on the file called SAFlashPlayer.exe and just close the white, empty window again.
The animations will start in a separate window.
How to play the videos: Just click on the blue camera icon:
How to play the Flash animations:
Go to beginning Pause Play
and play again
© Danfoss. The slideshow was made by Jørgen B Moller and Jens Andersen. Danfoss Sept. 2004
The Refrigerator.ppt
SAFlashPlayer.exe
Animations
CircuitExplanation.swf
condensing.wmv
Evaporation.wmv
Pump.wmv
PumpModel.swf
Spray.wmv

## Slide 2
What is inside?:
If you click on the refrigerator handle or the play button on the Flash animation, the refrigerator is stripped so we can see what is inside:
1 The "heart" of the refrigerator: The Compressor, which is working as a pump, not just controlling the circulation of the refrigerant, but also adding pressure to the circuit, which also makes the refrigerant hot.
Just like if you compress or pump air into a bicycle tube. You can sense the heat increase in the pump, while you pump and compress the air.
2 The Condenser sits on the back of the refrigerator, and is most likely quite dusty. The refrigerant is cooled down, and thereby it condensates, meaning the refrigerant turns liquid.
Just like humid air condensates on a cool surface
3 The Evaporator is placed inside the refrigerator, and is the part that makes the items in the refrigerator cold. It works as if you have a drop of alcohol, ether or another volatile liquid evaporating from your hand. You can sense the chilling from the evaporation (your hand is getting slightly colder)
4 The Thermostat controls the temperature by switching on-and-off the compressor, and thereby the cooling process. When the sensor (4a) senses that it is cold enough, it turns off the compressor, if it senses heat, it switches the compressor on.
Now click once again on the play button to see the process running.
What's inside?
Start animation

## Slide 3
The refrigerator
Inside a refrigerator a refrigerant, in liquid or gas form (phase) is circulating.
1 If we start by looking at the cold, evaporated gas, we use the compressor as a pump to compress the refrigerant. By compressing the gas, it heats up.
Just like if you compress or pump air into a bicycle tube. You can sense the heat increase in the pump, while you pump and compress the air.
2 The gas is now under higher pressure, and hot. The gas needs to be cooled. The black condenser is placed on the rear of the refrigerator, where the ambient air cools the gaseous refrigerant. When the gas now cools off (still under higher pressure) it condensates to liquid.
Just like humid air condensates on a cool surface
- When the compressor runs, the now liquid refrigerant will flow from the high-pressure area to the low-pressure area through the capillary tube, towards the evaporator.
5 To change from liquid to gas, the pressure where the refrigerant is placed, is reduced through an orifice (the capillary tube).
Just like what happens when you use an aerosol.
In comparison, the content of the aerosol is the pressure/liquid side, the orifice is the capillary tube, and the open space is the evaporator.
3 By changing from liquid to gas, the refrigerant evaporates and thereby cools the surroundings.
Just like if you have a drop of alcohol, ether or another volatile liquid evaporating on your hand. You can sense the chilling from the evaporation (your hand is getting slightly colder)
How does it work?
Start animation

## Slide 4
The refrigerant
Inside the refrigerator tubes a refrigerant, in liquid or gas form (phase) is circulating.
The refrigerant is kept under pressure in all parts of the refrigerator, although you have one part (the condenser) where the pressure is higher, than the other (the evaporator).
The refrigerant is usually a synthetic composition, although you could use, say, methane or butane.
The main idea is that you go from a high pressure, where the refrigerant is turned into liquid, that is, it condensates and another part where the pressure is reduced and the refrigerant turns into gas, that is, it evaporates.
The refrigerant
Start animation